## Slide 1
The activities were divided into two distinct development areas, namely star detection and centroid localization with dataset generation, assigned respectively to Sara Francavilla and Andreea Pollastri.
Task Overview:
Developing of an algorithm to overcome the star detection and centroid localization limitations of the open-source software LOST on a heterogeneous, noise-corrupted dataset.
Sara Francavilla – Andreea Pollastri
LOST
Final Results
Centroid Localization
Dataset Structure
Star Detection
Star Detection and Centroid Localization
in highly electrical and luminous noise systems
Work Division:

## Slide 2
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
LOST: A general view
Standing for Low-cost Open-Source Star Tracker, it is an open-source software suite for star tracking, developed for use on small, low-power, low-cost satellites like CubeSats.
More specifically:
Generates synthetic star images
Detects stars in real and synthetic images using classic image segmentation and thresholding techniques
Computes Centroids position based on a weighted average of pixel intensities
Identifies them through an onboard catalog
Determines spacecraft attitude

## Slide 3
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
LOST: Approaches
Star Detection
Pixels with intensity above a fixed threshold are selected.
Adjacent bright pixels are grouped into connected components (blobs).
Each blob is treated as a star candidate.
Centroid localization
Uses a center-of-gravity (intensity-weighted average) over the detected star blob.
Assumes stars are compact and approximately symmetric.
Centroid accuracy depends strongly on the quality of star detection and on noise contamination within the blob.

## Slide 4
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
LOST: Limitations
Noise peaks often incorrectly detected as star candidates.
No Gaussian shape analysis.
Performance degrades in the presence of strong noise or elongated (stretched) stars.
Background noise and dark current bias the centroid toward brighter noise pixels.
Blurred or elongated stars produce systematic centroid shifts.
No explicit modeling of the star intensity distribution or noise statistics.

## Slide 5
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Study Images and Characteristics

## Slide 6
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Study Images and Characteristics

## Slide 7
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Setting Threshold
80% background
Ground Truth: 322
Image1 – 312 peaks
Image2 – 312 peaks
Image3 – 9021 peaks
Image4 – 8797 peaks
Image5 – 9041 peaks
Image6 – 9041 peaks
Image7 – 9050 peaks

## Slide 8
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Studying Histograms
Aligning peak to perfect image peak

## Slide 9
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Studying Histograms
Soft thresholding

## Slide 10
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Denoised Results

## Slide 11
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Static Nested Windows Function
def detect_stars_nested_base(img, A_size=3, B_size=7, th_mean=2, th_std=1):

## Slide 12
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Studying Windows Parameters
Changing Windows Dimensions
Changing Mean and StD Thresholds

## Slide 13
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Multiscale Windows Function
def detect_stars_multiscale(img, A_sizes=[3,5,7], B_sizes=[7,11,15],
th_mean=4, th_std=3):
True Positives: 20
False Positives: 0
False Negatives: 302 Precision: 100.00%
Recall: 6.21%
F1-Score: 11.70%
True Positives: 15
False Positives: 0
False Negatives: 306 Precision: 100.00%
Recall: 4.67%
F1-Score: 8.93%
True Positives: 20
False Positives: 0
False Negatives: 302 Precision: 100.00%
Recall: 6.21%
F1-Score: 11.70%

## Slide 14
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Adaptive Multiscale Function
Image 6 (stretched):
Standard: 10 stars detected Adaptive: 21 stars detected
Improvement:
+11 stars (110.0%)
Image 7 (noisy and stretched): Standard: 1 stars detected Adaptive: 2 stars detected
Improvement:
+1 stars (100.0%)
def detect_stars_multiscale_adaptive(img, A_sizes=[3,5,7],sizes=[7,11,15],
th_mean=3, th_std=2, adapt_eccentricity=True,
ecc_threshold=0.4, scale_eccentricity_factor=0.5):

## Slide 15
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Improving Detection

## Slide 16
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Improving Detection
Setting eccentricity threshold to mode (frequency peak)

## Slide 17
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Improving Detection
True Positives: 17
False Positives: 4
False Negatives: 305
Precision: 80.95%
Recall: 5.28%
F1-Score: 9.91%
True Positives: 1
False Positives: 1
False Negatives: 311
Precision: 50.00%
Recall: 0.32%
F1-Score: 0.64%

## Slide 18
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Star Detection: Final Detection Workflow
Estimate noise and blur
IF noisy → denoise
IF blurred → adaptive multiscale detection
ELSE → multiscale detection
ELSE
IF clean → local maxima
ELSE → adaptive multiscale detection
RETURN stars

## Slide 19
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Dataset Structure
Composed by synthetic star-field images generated by varying sky position (RA, DEC, ROLL) and imaging conditions.
Stars are always visible to the naked eye while noise, blur, and dark current simulate realistic scenarios.
AAA0–AAA6 → same sky position, different noise levels
Up to 26³ unique sky positions
Ground-truth centroids stored in dataset/centroid/centroid_<IMAGE_ID>.csv

## Slide 20
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization
The spatial distribution of a star is described by the Point Spread Function

## Slide 21
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization
We compare a single real star patch extracted from the image with the estimated system PSF.
Image with atmospere:

## Slide 22
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization
We compare a single real star patch extracted from the image with the estimated system PSF.
Image with noise:

## Slide 23
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization
We compare a single real star patch extracted from the image with the estimated system PSF.
Image with blur:

## Slide 24
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization:
Local Compensation
Technique used to reduce the effect of noise and local intensity variations on star centroid estimation.
Where G_Var is the variance of the neighborhood,
G8, G7 are the maximum and sub-maximum gray values,
G1, G2 are the minimum and sub-minimum gray values.

## Slide 25
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization:
Local Compensation

## Slide 26
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization:
Local Compensation

## Slide 27
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization:
Mathematically
To estimate the star center from the image, we use a weighted centroid approach with a threshold.
weights = patch – T
xc = np.sum((xx + x1) * weights) / np.sum(weights)
yc = np.sum((yy + y1) * weights) / np.sum(weights)

## Slide 28
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization:
Algorithm
patches → extract_star_patches(size=window)
FOR every patch
patch → energy_compensation
T → patch.min() + percent * (patch.max() - patch.min())
c → threshold_centroid
centroid.append(c)
Hyperparameters:
percent = 0.2
window = 5

## Slide 29
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization:
Algorithm error - 3px
Image | TP | FP | FN | Precision | Recall | Stars
0 | 110 | 188 | 83 | 0.3691 | 0.5699 | 298
1 | 164 | 133 | 29 | 0.5522 | 0.8497 | 297
2 | 9 | 13 | 184 | 0.4091 | 0.0466 | 22
3 | 7 | 18 | 186 | 0.2800 | 0.0363 | 25
4 | 9 | 10 | 184 | 0.4737 | 0.0466 | 19
5 | 4 | 17 | 189 | 0.1905 | 0.0207 | 21
6 | 1 | 3 | 192 | 0.2500 | 0.0052 | 4

## Slide 30
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization:
Algorithm Duplicated Coordinates
patches → extract_star_patches(size=window)
FOR patch in patches
patch → energy_compensation
patch → extract_patch(size=window_s)
T → patch.min() + percent * (patch.max() - patch.min())
c → threshold_centroid
centroid.append(c)
FOR i in centroid
IF i in used CONTINUE
cluster = [i]
FOR j in centroid
IF j not in used AND distance(i, j) < 1.5
cluster.append(j)
final.append(mean(cluster))
Hyperparameters:
window = 5
window small = 3
percent small = 0.8

## Slide 31
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Centroid Localization:
Algorithm error - 3px
Image |  | TP | FP | FN | Precision | Recall | Stars
0 |  | 120 | 178 | 73 | 0.4027 | 0.6218 | 298
1 |  | 171 | 126 | 22 | 0.5758 | 0.8860 | 297
2 |  | 10 | 0 | 183 | 1.0000 | 0.0518 | 10
3 |  | 8 | 7 | 185 | 0.5333 | 0.0415 | 15
4 |  | 9 | 1 | 184 | 0.9000 | 0.0466 | 10
5 |  | 4 | 8 | 189 | 0.3333 | 0.0207 | 12
6 |  | 2 | 2 | 191 | 0.5000 | 0.0104 | 4
The number of stars decreases after the consolidation step.

## Slide 32
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Final Results: Star Detection
Categories 0–2 (clean / mild noise):
Both methods achieve high precision.
LOST performs optimally in ideal conditions.
Categories 3–4 (high noise, dark current):
LOST precision degrades due to increasing false positives.
The proposed method maintains precision >90%.
Category 5 (blur):
LOST fails dramatically (precision 2.49%) due to noise and blur peaks.
The proposed method remains stable and reliable.
Category 6 (blur + dark current):
Proposed method continues to control false detections.
LOST shows unstable behavior.

## Slide 33
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Final Results: Star Detection
Recall decreases for both methods as noise increases.
Degradation is strongest in severely noisy and blurred categories.
The proposed method achieves comparable or slightly higher recall than LOST in most classes.

## Slide 34
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Final Results: Star Detection
F1-score drops in highly degraded images due to recall loss.
Despite this, the proposed method consistently achieves higher F1-scores than LOST across most categories.

## Slide 35
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Final Results: Centroid Localization
Categories 0–1 (ideal / low noise):
LOST slightly outperforms due to its role in image generation.
Categories 2–4 (moderate noise, dark current):
The proposed method achieves comparable or higher numbers of correct matches.
Category 5 (blur):
LOST reports an artificially high number of matches caused by over-detection.
The proposed method remains consistent and realistic.
Category 6 (blur + dark current):
Both methods show similarly low performance.

## Slide 36
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Final Results: Centroid Localization
Category 0 (noise-free):
LOST achieves perfect localization.
Noisy categories (1–6):
Match ratio decreases for both methods as star visibility degrades.
The proposed method generally achieves equal or higher match ratios in noisy conditions.

## Slide 37
Sara Francavilla – Andreea Pollastri
Star Detection and Centroid Localization
Final Results: Centroid Localization
Measures the proportion of correct centroids among detected stars.
Across most categories:
The proposed method shows higher and more stable relative ratios.
Category 5 (blur):
LOST suffers a strong drop due to excessive false detections.

## Slide 38
Sara Francavilla – Andreea Pollastri
LOST
Final Results
Centroid Localization
Dataset Structure
Star Detection
Thanks
Star Detection and Centroid Localization